## Slide 1: The Processor
Dr. Rajib Ranjan Maiti
CSIS, BITS-Pilani, Hyderabad
Disclaimer: To know the complete syllabus, handout and the text book should be consulted

## Slide 2: A Basic MIPS Implementation
We shall examine an implementation of some of MIPS instructions
  load word (lw) and store word (sw)
  Arithmetic: add, sub, AND, OR, and slt
  branch equal (beq) and jump (j)
Our focus
  the key principles used in creating a datapath and designing the control
How the instruction set architecture determines different aspects of the implementation?
How the implementation affects the clock rate and CPI for the computer?

## Slide 3: MIPS implementation: functional units and their interconnection

## Slide 4: The datapath of MIPS implementation

## Slide 5: Logic Design Conventions
Two questions
  how the hardware logic will operate?
  how the computer is clocked?
two different types of logic elements:
  elements that operate on data values : combinational, which means that their outputs depend only on the current inputs, e.g., ALU
  elements that contain state: contain state, i.e., it has some internal storage, e.g., the instruction and data memories, as well as the registers
In addition to flip-flops, MIPS implementation uses
  two other types of state elements: memories and registers,

## Slide 6: Logic Design Conventions
At any time, the clock is used to determine
  when the state element should be written or
  a state element can be read
Clocking Methodology defines
  when signals can be read and when they can be written
We will assume an edge-triggered clocking methodology, i.e.,
  any values stored in a sequential logic element are updated only on a clock edge
  Because only state elements can store a data value, any collection of combinational logic must have its inputs come from a set of state elements and its outputs written into a set of state elements
  The inputs are values that were written in a previous clock cycle, while the outputs are values that can be used in a following clock cycle

## Slide 7
Finally, color indicates a control signal as opposed to a signal that carries data

## Slide 8: Building a Datapath

## Slide 9: Datapath for Instruction fetch
to start a datapath design
  examine the major components required to execute each class of MIPS instructions
Some Components are required for every instruction : instruction fetch
A memory unit
  stores the instructions of a program
  supplies an instruction given an address
The program counter (PC)
  a register that holds the address of the current instruction
An adder
  to increment the PC to the address of the next instruction

## Slide 11: How do we combine these datapath elements?

## Slide 12: Building a Datapath: Execution of R-Type instruction
The task
  Read two registers,
  perform an ALU operation on the contents of the registers, and
  write the result to a register
Example of R-Type instructions
  add, sub, AND, OR, and slt
MIPS elements
  32 general-purpose registers are stored in a structure called a register file
  An ALU to operate on the values read from the registers

## Slide 14: Building a Datapath: Execution of Load and Store
MIPS elements
  the register file
  the ALU
  a unit to sign-extend the 16-bit off set field in the instruction to a 32-bit signed value,
  a data memory unit

## Slide 16: Building a Datapath: Branch instruction

## Slide 17: Building a Datapath: Branch instruction
Reverse to Compute Label:
Temp1 = Branch Target – (PC + 4)
Temp2 = RightShift2 (temp1)
Label = SignReduce16(Temp2)

## Slide 18: Building a Datapath: Jump instruction
The jump instruction
  operates by replacing the lower 28 bits of the PC with the lower 26 bits of the instruction shifted left by 2 bits
  Simply concatenating 00 to the jump off set accomplishes this shift

## Slide 19: Creating a Single Datapath: Memory and R-Type
This simplest datapath will attempt to execute all instructions in one clock cycle.
This means that no datapath resource can be used more than once per instruction,
So, any element needed more than once must be duplicated

## Slide 20: Detailed MIPS Architecture

## Slide 21: A Simple Implementation Scheme

## Slide 22: An implementation of our MIPS subset
  The MIPS ALU defines the 6 following combinations of four control inputs:
  Depending on the instruction class, the ALU needs to perform one of the first five functions
  For the R-type instructions,
    the ALU needs to perform one of the five actions (AND, OR, subtract, add, or set on less than),
    The actions depends on 6-bit funct (or function) value
ALU control lines | Function
0000 | AND
0001 | OR
0010 | Add
0110 | Subtract
0111 | set on less than
1100 | NOR

## Slide 24: Designing the Main Control Unit
let’s identify the fields of an instruction and the control lines that are needed for the datapath we constructed

## Slide 25: Review the formats of the three instruction classes
The op field, also called the opcode,
  always contained in bits 31:26
The two registers to be read
  always specified by the rs (25:21) and rt (20:16) fields
  This is true for the R-type instructions, branch equal, and store
The base register for load and store instructions
  always in rs (25:21)
The 16-bit off set for branch equal, load, and store
  always in positions 15:0
The destination register
  one of two places
  For a load it is in bit positions 20:16 (rt),
  for an R-type instruction it is in bit positions 15:11 (rd)
  Therefore, we will need to add a multiplexor

## Slide 26: The Datapath
seven single-bit control lines plus the 2-bit ALUOp control
signal

## Slide 27: 7 control lines

## Slide 28: Datapath with control lines

## Slide 29: everything occurs in one clock cycle

## Slide 30: Operation of the Datapath
How about the execution of a load word, such as
  lw $t1, offset($t2)
a load instruction is operating in five steps
  An instruction is fetched from the instruction memory, and the PC is incremented
  A register ($t2) value is read from the register file
  The ALU computes the sum of the value read from the register file and the sign-extended, lower 16 bits of the instruction (offset)
  The sum from the ALU is used as the address for the data memory
  The data from the memory unit is written into the register file; the register destination is given by bits 20:16 of the instruction ($t1)

## Slide 32: Operation of the Datapath
How about the execution of a beq, such as
  beq $t1, $t2, offset
a beq instruction is operating in four steps
  An instruction is fetched from the instruction memory, and the PC is incremented
  Two registers, $t1 and $t2, are read from the register file
  The ALU performs a subtract on the data values read from the register file
    The value of PC + 4 is added to the sign-extended, lower 16 bits of the instruction (offset) shifted left by two; the result is the branch target address
  The Zero result from the ALU is used to decide which adder result to store into the PC

## Slide 33: Data path for beq t1, t2, offset

## Slide 34: let’s add the jump instruction to show how the basic datapath and control can be extended

## Slide 35: Datapath for j address