## Slide 1: Dependability, reliability, availability I/O performance measures Redundant Array of Independent Disks (RAID)
Dr R. R. Maiti
CSIS, BITS-Pilani, Hyderabad

## Slide 2: Defining Failure
We start with an assumption that
  you have a specification of proper service
Users can then see a system alternating between two states of delivered service with respect to the service specification:
  1. Service accomplishment, where the service is delivered as specified
  2. Service interruption, where the delivered service is different from the specified service

## Slide 3: Defining Reliability
Reliability
  a measure of the continuous service accomplishment—or, equivalently, of the time to failure—from a reference point.
Hence, mean time to failure (MTTF) is a reliability measure
A related term is annual failure rate (AFR)
  the percentage of devices that would be expected to fail in a year for a given MTTF
When MTTF gets large it can be misleading,
  while AFR leads to better intuition

## Slide 4: Example: MTTF vs. AFR of Disks
Some disks today are quoted to have a 1,000,000-hour MTTF.
  As 1,000,000 hours is 1,000,000/(365 x 24) = 114 years,
    it would seem like they practically never fail
  Warehouse scale computers that run Internet services such as Search might have 50,000 servers.
  Assume each server has 2 disks.
  Use AFR to calculate how many disks we would expect to fail per year

## Slide 5: Example: MTTF vs. AFR of Disks
One year is 365 x 24 = 8760 hours.
A 1,000,000-hour MTTF means an AFR of 8760/1,000,000 = 0.00876 = 0.876%.
With 100,000 disks, we would expect 876 disks to fail per year, or on average more than 2 disk failures per day!
Some disks today are quoted to have a 1,000,000-hour MTTF.
  As 1,000,000 hours is 1,000,000/(365 x 24) = 114 years,
    it would seem like they practically never fail
  Warehouse scale computers that run Internet services such as Search might have 50,000 servers.
  Assume each server has 2 disks.
  Use AFR to calculate how many disks we would expect to fail per year

## Slide 6: Service interruption
Service interruption is measured as
  mean time to repair (MTTR)
Mean time between failures (MTBF)
  MTBF = MTTF + MTTR
Although MTBF is widely used,
  MTTF is often the more appropriate term
Availability is then
  a measure of service accomplishment with respect to the alternation between the two states of accomplishment and interruption
Availability is statistically quantified as
  Availability = MTTF/ (MTTF + MTTR)

## Slide 7: Quality of the components
To increase MTTF,
  you can improve the quality of the components or design systems to continue operation in the presence of components that have failed
Hence, failure needs to be defined with respect to a context
  failure of a component may not lead to a failure of the system
To make this distinction clear,
  the term fault is used to mean failure of a component
Here are three ways to improve MTTF:
  1. Fault avoidance: Preventing fault occurrence by construction.
  2. Fault tolerance: Using redundancy to allow the service to comply with the service specification despite faults occurring.
  3. Fault forecasting: Predicting the presence and creation of faults, allowing the component to be replaced before it fails

## Slide 8: The Hamming Single Error Correcting, Double Error Detecting Code (SEC/DED)
Richard Hamming invented a popular redundancy scheme for memory,
  for which he received the Turing Award in 1968.
Hamming distance
  the minimum number of bits that are different between any two correct bit patterns
  For example, the distance between 011011 and 001111 is two.
What happens if the minimum distance between members of a codes is two, and we get a one-bit error?
  It will turn a valid pattern in a code to an invalid one.
  Thus, if we can detect whether members of a code are valid or not, we can detect single bit errors, and can say we have a single bit error detection code.
  Hamming used a parity code for error detection.
  In a parity code, the number of 1s in a word is counted; the word has odd parity if the number of 1s is odd and even otherwise.
  When a word is written into memory, the parity bit is also written (1 for odd, 0 for even).
  That is, the parity of the N+1 bit word should always be even.
  Then, when the word is read out, the parity bit is read and checked.
  If the parity of the memory word and the stored parity bit do not match, an error has occurred

## Slide 9: Example:
Calculate the parity of a byte with the value 31ten and show the pattern stored to memory.
  Assume the parity bit is on the right.
  Suppose the most significant bit was inverted in memory, and then you read it back.
  Did you detect the error? What happens if the two most significant bits are inverted?

## Slide 10: Example:
Calculate the parity of a byte with the value 31ten and show the pattern stored to memory.
  Assume the parity bit is on the right.
  Suppose the most significant bit was inverted in memory, and then you read it back.
  Did you detect the error? What happens if the two most significant bits are inverted?
31ten = (0001 1111)two,  five 1s.
To make parity even, we need to write a 1 in the parity bit, i.e., (0001 1111 1)two.
If the most significant bit is inverted when we read it back, i.e 100111111two  seven 1s.
Since we expect even parity and calculated odd parity, we would signal an error.
If the two most significant bits are inverted, i.e., (1101 1111 1)two  eight 1s or even parity  we would not signal an error

## Slide 11: parity code
a parity code cannot correct errors
  Hamming wanted to do as well as detect them
If we used a code that had a minimum distance of 3,
  then any single bit error would be closer to the correct pattern than to any other valid pattern.
He came up with an easy to understand mapping of data into a distance 3 code
  Hamming Error Correction Code (ECC)
We use extra parity bits to allow the position identification of a single error

## Slide 12: Hamming ECC
1. Start numbering bits from 1 on the left
2. Mark all bit positions that are powers of 2 as parity bits
  i.e., positions 1, 2, 4, 8, 16, …
3. All other bit positions are used for data bits
  i.e., positions 3, 5, 6, 7, 9, 10, 11, 12, 13, 14, 15, …
4. The position of parity bit determines sequence of data bits that it checks is:
  ■ Bit 1 (0001two) checks bits (1,3,5,7,9,11,...),
    which are bits where rightmost bit of address is 1 (0001two, 0011two, 0101two, 0111two, 1001two, 1011two,…)
  ■ Bit 2 (0010two) checks bits (2,3,6,7,10,11,14,15,…),
    which are the bits where the second bit to the right in the address is 1
  ■ Bit 4 (0100two) checks bits (4–7, 12–15, 20–23,...),
    which are the bits where the third bit to the right in the address is 1
  ■ Bit 8 (1000two) checks bits (8–15, 24–31, 40–47,...),
    which are the bits where the fourth bit to the right in the address is 1
  Note that each data bit is covered by two or more parity bits
5. Set parity bits to create even parity for each group

## Slide 13: Hamming ECC

## Slide 14: Hamming ECC code
Assume one byte data value is (1001 1010)two.
  First show the Hamming ECC code for that byte, and then invert bit 10 and show that the ECC code finds and corrects the single bit error
Leaving spaces for the parity bits, the 12 bit pattern is _ _ 1 _ 0 0 1 _ 1 0 1 0.
Position 1 checks bits 1,3,5,7,9, and11, which we highlight: __ 1 _ 0 0 1 _ 1 0 1 0.
To make the group even parity, we should set bit 1 to 0.
Position 2 checks bits 2,3,6,7,10,11, which is 0 _ 1 _ 0 0 1 _ 1 0 1 0  odd parity, so we set position 2 to a 1.
Position 4 checks bits 4,5,6,7,12, which is 0 1 1 _ 0 0 1 _ 1 0 1 0,  we set fourth position to a 1.
Position 8 checks bits 8,9,10,11,12, which is 0 1 1 1 0 0 1 _ 1 0 1 0,  we set eighth position to a 0.
The final code word is 0111 0010 1010.
Inverting bit 10 changes it to 0111 0010 1110.
Parity bit 1 is 0 (011100101110 is four 1s, so even parity; this group is OK).
Parity bit 2 is 1 (011100101110 is five 1s, so odd parity; there is an error somewhere).
Parity bit 4 is 1 (011100101110 is two 1s, so even parity; this group is OK).
Parity bit 8 is 1 (011100101110 is three 1s, so odd parity; there is an error somewhere).
Parity bits 2 and 10 are incorrect. As 2 + 8 = 10, bit 10 must be wrong.
Hence, we can correct the error by inverting bit 10: 011100101010. Voila!

## Slide 15: correct single bit and detect double bit
Hamming did not stop at single bit error correction code.
At the cost of one more bit,
  we can make the minimum Hamming distance in a code be 4.
  This means we can correct single bit errors and detect double bit errors.
The idea is to add a parity bit that is calculated over the whole word.
Let’s use a four-bit data word as an example,
  which would only need 7 bits for single bit error detection.
Hamming parity bits H (p1 p2 p3) are computed (even parity as usual) plus the even parity over the entire word, p4:
  1 2 3 4 5 6 7 8
  p1 p2 d1 p3 d2 d3 d4 p4

## Slide 16: correct one and detect two
calculate parity over the ECC groups (H) as before plus one more over the whole group (p4 ).
There are four cases:
  1. H is even and p4 is even, so no error occurred.
  2. H is odd and p4 is odd, so a correctable single error occurred.
    (p4 should calculate odd parity if one error occurred.)
  3. H is even and p4 is odd, a single error occurred in p4 bit, not in the rest of the word, so correct the p4 bit.
  4. H is odd and p4 is even, a double error occurred.
    (p4 should calculate even parity if two errors occurred.)
Single Error Correcting / Double Error Detecting (SEC/DED)
  common in memory for servers today
Conveniently, eight byte data blocks can get SEC/DED with just one more byte, which is why many DIMMs are 72 bits wide.

## Slide 17: RAID (6e)

## Slide 18: Capacity
Improvement in capacity is customarily expressed as
  improvement in areal density, measured in bits per square inch:
  Areal density = (Tracks/ Inch) on a disk surface x (Bits / Inch) on a track

## Slide 19: Disk Power
Power is an increasing concern for disks as well as for processors.
A typical ATA disk in 2011 might use
  9 watts when idle,
  11 watts when reading or writing, and
  13 watts when seeking
Because it is more efficient to spin smaller mass,
  smaller diameter disks can save power.
One formula that indicates
  the importance of rotation speed and the size of the platters for the power consumed by the disk motor is the following [Gurumurthi et al. 2005]:
  Power = Diameter^4.6 x RPM^2.8 x Number of platters

## Slide 20: Redundant Array of Inexpensive (or Independent) Disks (RAID)
The standard RAID levels are well documented, so we will just do a quick review here and discuss advanced levels in more depth.
RAID 0—
  It has no redundancy and is sometimes nicknamed JBOD, for just a bunch of disks, although the data may be striped across the disks in the array.
  This level is generally included to act as a measuring stick for the other RAID levels in terms of cost, performance, and dependability
RAID 1—
  Also called mirroring or shadowing, there are two copies of every piece of data.
  It is the simplest and oldest disk redundancy scheme, but it also has the highest cost.
  Some array controllers will optimize read performance by allowing the mirrored disks to act independently for reads, but this optimization means it may take longer for the mirrored writes to complete

## Slide 21: Redundant Array of Inexpensive (or Independent) Disks (RAID)
RAID 2—
  This organization was inspired by applying memory-style error correcting codes (ECCs) to disks.
  It was included because there was such a disk array product at the time of the original RAID paper, but none since then as other RAID organizations are more attractive.
RAID 3—
  Since the higher-level disk interfaces understand the health of a disk, it’s easy to figure out which disk failed.
  Designers realized that if one extra disk contains the parity of the information in the data disks, a single disk allows recovery from a disk failure.
  The data are organized in stripes, with N data blocks and one parity block.
  When a failure occurs, we just “subtract” the good data from the good blocks, and what remains is the missing data.
  RAID 3 assumes that the data are spread across all disks on reads and writes, which is attractive when reading or writing large amounts of data.

## Slide 22: Redundant Array of Inexpensive (or Independent) Disks (RAID)
RAID 4—
  Many applications are dominated by small accesses.
  Since sectors have their own error checking, you can safely increase the number of reads per second by allowing each disk to perform independent reads.
  It would seem that writes would still be slow, if you have to read every disk to calculate parity.
  To increase the number of writes per second, an alternative approach involves only two disks.
  First, the array reads the old data that are about to be overwritten, and then calculates what bits would change before it writes the new data.
  It then reads the old value of the parity on the check disks, updates parity according to the list of changes, and then writes the new value of parity to the check disk.
  Hence, these so-called “small writes” are still slower than small reads— they involve four disks accesses—but they are faster if you had to read all disks on every write.
  RAID 4 has the same low check disk overhead as RAID 3, and it can still do large reads and writes as fast as RAID 3 in addition to small reads and writes, but control is more complex.

## Slide 23: Redundant Array of Inexpensive (or Independent) Disks (RAID)
RAID 5—
  Note that a performance flaw for small writes in RAID 4 is that they all must read and write the same check disk, so it is a performance bottleneck.
  RAID 5 simply distributes the parity information across all disks in the array, thereby removing the bottleneck.
  The parity block in each stripe is rotated so that parity is spread evenly across all disks.
  The disk array controller must now calculate which disk has the parity for when it wants to write a given block, but that can be a simple calculation.
  RAID 5 has the same low check disk overhead as RAID 3 and 4, and it can do the large reads and writes of RAID 3 and the small reads of RAID 4, but it has higher small write bandwidth than RAID 4.
  Nevertheless, RAID 5 requires the most sophisticated controller of the classic RAID levels.

## Slide 24
RAID levels, their fault tolerance, and their overhead in redundant disks. The paper that introduced the term RAID [Patterson, Gibson, and Katz 1987] used a numerical classification that has become popular. In fact, the nonredundant disk array is often called RAID 0, indicating that the data are striped across several disks but without redundancy. Note that mirroring (RAID 1) in this instance can survive up to eight disk failures provided only one disk of each mirrored pair fails; worst case is both disks in a mirrored pair fail. In 2011, there may be no commercial implementations of RAID 2; the rest are found in a wide range of products. RAID 0+ 1, 1 + 0, 01, 10, and 6 are discussed in the text.
RAID level | Disk failures tolerated, check space overhead for 8 data disks | Pros | Cons | Company products
0 Nonredundant striped | 0 failures, 0 check disks | No space overhead | No protection | Widely used
1 Mirrored | 1 failure, 8 check disks | No parity calculation; fast recovery; small writes faster than higher RAIDs; fast reads | Highest check storage overhead | EMC, HP (Tandem), IBM
2 Memory-style ECC | 1 failure, 4 check disks | Doesn’t rely on failed disk to self-diagnose | ~Log 2 check storage overhead | Not used
3 Bit-interleaved parity | 1 failure, 1 check disk | Low check overhead; high bandwidth for large reads or writes | No support for small, random reads or writes | Storage Concepts
4 Blockinterleaved parity | 1 failure, 1 check disk | Low check overhead; more bandwidth for small reads | Parity disk is small write bottleneck | Network Appliance
5 Blockinterleaved distributed parity | 1 failure, 1 check disk | Low check overhead; more bandwidth for small reads and writes | Small writes4 disk accesses | Widely used
6 Row-diagonal parity, EVENODD | 2 failures, 2 check disks | Protects against 2 disk failures | Small writes6 disk accesses; 2 check overhead | Network Appliance

## Slide 25: two levels that have become popular
RAID 10 versus 01 (or 1 +0 versus RAID 0+1)
One topic not always described in the RAID literature involves how mirroring in RAID 1 interacts with striping.
Suppose you had, say, four disks’ worth of data to store and eight physical disks to use.
  Would you create four pairs of disks—each organized as RAID 1—and then stripe data across the four RAID 1 pairs?
  Alternatively, would you create two sets of four disks—each organized as RAID 0—and then mirror writes to both RAID 0 sets?
  The RAID terminology has evolved to call the former RAID 1 + 0 or RAID 10 (“striped mirrors”) and the latter RAID 0 + 1 or RAID 01 (“mirrored stripes”).

## Slide 26: two levels that have become popular
RAID 6:
  Beyond a Single Disk Failure
    The parity-based schemes of the RAID 1 to 5 protect against a single self identifying failure; however, if an operator accidentally replaces the wrong disk during a failure, then the disk array will experience two failures, and data will be lost.
  Another concern is that since disk bandwidth is growing more slowly than disk capacity, the MTTR of a disk in a RAID system is increasing, which in turn increases the chances of a second failure.
For example,
  a 500 GB SATA disk could take about 3 hours to read sequentially assuming no interference.
  Given that the damaged RAID is likely to continue to serve data, reconstruction could be stretched considerably, thereby increasing MTTR.
Besides increasing reconstruction time,
  another concern is that reading much more data during reconstruction means increasing the chance of an uncorrectable media failure, which would result in data loss.
  Other arguments for concern about simultaneous multiple failures are the increasing number of disks in arrays and the use of ATA disks, which are slower and larger than SCSI disks